## Slide 1: An intoduction to the Auto-scrutineer
Contents
New submission folder structure
Basic overview
  Rule types
  Explanation and examples
In-depth overview (wip)
Rule definitions (wip)
VTK-pipelines (wip)
Disclaimer:
I am NOT a software engineer, so set your expectations accordingly.
Please let me know if there are critical bug/errors in my code, or other areas that might be improved.
Part 1
Relevant to everyone
Part 2
Mostly relevant to staff and maintainers
(but everyone is welcome)

## Slide 2: Part 1
This part is relevant to everyone, competitors, staff etc.
please familiarize yourself with the content.

## Slide 3: New submission folder structure
Competitors must specify which .stl’s are considered floor, frontwing etc.
Old structure
📁MyRacingTeam_Round1_v2
│
├─ 📁 high_res_surfaces
│ ├─ FW_endplate.stl
│ ├─ FW_flap.stl
│ ├─ rearwing.stl
│ └─ etc
│
├─ 📁 vehicle_body
│ ├─ body.stl
│ ├─ nose.stl
│ ├─ mirror_strut.stl
│ └─ etc
│
└─ 📁 etc
└─ etc
New submission folder
📁MyRacingTeam_Round1_v2
│
├─ 📁 frontwing_flaps
│ ├─ FW_flap_1.stl
│ └─ FW_flap_2.stl
│
├─ 📁 frontwing_mainplane
│ └─ fw_mp.stl
│
├─ 📁 main_floor
│ └─ floor_v13_revK_final2.stl
│
└─ 📁 etc
└─ etc
In the new structure there is a folder for each ”part” referenced in the rules.
Each folder can contain multiple stls.
So, more folders but no ambiguity about which stls belong to which parts.
Full list of parts should be specified in the rules.
After scrutineering, the .stl files are copied to a new "input_file" folder following the "old structure," making the submission "MFlow ready."

## Slide 4: Rule types
Currently supported “rule types”:
Obscure (read: to conceal etc.)
Number of sections
Top/bottom visibility
Bounding box size (not currently in use)
Things like “10 mm rule” and “no floating parts” cannot be checked with this tool. If someone has ideas on how check these, please share them.

## Slide 5: Obscure rule
The obscure rule is quite versatile. It can be used to test a range of different rules. These include:
- Part-X must be fully contained within RV-Y
- From *angle* Part-X must obscure RS-Y
- Part-Y must be lowest part of the car within *area*
Common for all these rules is that if X is visible from a certain angle, then that indicates a breach of the rule.
Two different geometries must be specified:
“given_geometry” (X in the examples above)
“ref_geometry” (Y in the example above)
An additional ”mask” geometry can also be specified. The mask can help to specify the *area* in the example above.
When checking this rule, a scene is created where the given geometry is colored red, and the reference geometry is colored black. Images of this scene are rendered. You can now check the rendered images for red pixels. Any red pixel = illegal geometry.
If an infringement is found, then the color palette is altered slightly, and an image is saved that more clearly shows the infringement (see example next slide)
To avoid Z-fighting issues, 6 copies of the reference geometry are added to the scene. Each translated 1 mm along –x, +x, -y, +y, -z and +z respectively

## Slide 6: Obscure rule, example
What the rule-checker sees:
(flat-coloring)
Rendered for more clarity:
(rendered with shadows and transparent reference)
Red = illegal
The bottom surface of the mainplane is not fully contained within the RV

## Slide 7: Number of sections
”Number of sections” –rule can be used to count number of sections in frontwings, rearwings etc.
It works by cutting the geometry with a number of planes. The planes are defined with a normal vector, and an origin point.
The normal vector is specified in the rules.
for example (0, 1, 0) for y-sections.
The origin points can be defined either as a strict list of specific points, or as a ”semi-random” list of points in an interval. For semi-random sampling a ”maximum unprobed interval” is given, this is the maximum distance between planes in the sampling_interval.
The 3d coordinates of the origin points are found by multiplying each scalar in the list with the normal vector of the plane.
An image of the cut section is rendered. Then the number of sections visible in the image are counted. (see next slide)
NB! Since it only checks a limited number of sections, small infringements may or may not be caught!
Rendered image of a section:

## Slide 8: Number of sections
The function counts the number of sections in the rendered image, with the following method:
(8bit RGBa array)
(Boolean array)
Convert to B/W
”Bucket fill” with white from a corner
Find a black pixel,
Bucket fill from this pixel
Add one to the counter
Repeat until image is all white
Rendered cut section
(red frame added for clarity)
Why this way?
Another method could be to simply count the number of red sections. I decided against this approach because you often have overlapping geometries (because it is good for meshing). You don't want to count these overlapping regions as a section. This way you only count the number of sections in contact with the external flow. Imo this is closer to ideal.
Result: 2 sections

## Slide 9: Top/bottom visibility
Top/bottom visibility checks that every surface of the part is either visible from above or below. This rule takes sections of the given geometry, like the number of sections rule, but processes the images differently.
After ”bucket-filling” from a corner, it looks at every column of pixels in the image. Specifically, it counts the number of times the pixel value changes from black to white or white to black. If it counts more than 2 of these intersections then that suggest some overhang, and that means some surfaces must not be visible from above or below.
(8bit RGBa array)
(Boolean array)
Convert to B/W
”Bucket fill” with white from a corner
Rendered cut section
(red frame added for clarity)
(this is a bad example, because top/bottom visibility doesn’t apply to the wings…)

## Slide 10: Part 2
Mostly relevant to staff/contributors
This part should be mostly irrelevant to competitors that don’t wish to contribute to the script.

## Slide 11: Rule definition
All rules are gathered in a single list. This list is defined in rules.py
Each rule is defined as a dictionary
The rule-checker iterates through the list of rules. The keyword: ”rule_type” is important, this specifies which “rule-function” is called.
All rules must return a string that is added to the report.
New rules can be added by simply defining a new function and adding this function to the if-statement in the scrutineer function.
Two different rules in the rules list
From scrutineer function:

## Slide 12: Obscure rule definition
Rule section name is used for the report
Angles, specifies the camera angles. Options include ”all”, ”above”, ”below” etc. See camera_funs.py for more info
Ref_geometry is colored black
Given geometry is colored red
Focus specifies the part to focus the camera on, here the given geometry.
Geometries can be combined by supplying a list of parts instead of a string. This functionality replaces the ”masks” used in previous versions, because this is better

## Slide 13: Overview of generic VTK-pipeline (for reference)
Source
Mapper
Interactor
Renderer
RenderWindow
Actor
Not used here

## Slide 14: Overview of VTK-pipeline for Obscure rule
Mapper
Render to numpy array
Renderer
RenderWindow
vtkAppend-PolyData
Actor
Stl reader
Convert to vtkPolyData
Stl reader
Convert to vtkPolyData
Stl reader
Convert to vtkPolyData
…
Get Bounding Box coordinates
Define camera focus and location
Read all stls in a given folder
Bounding box coordinates are now (march 2025) found from the actor

## Slide 15: Overview of VTK-pipeline for N sections rule and top/bottom visibility rule
Stl reader
Convert to vtkPolyData
Get Bounding Box coordinates
Define camera focus and location
Actor
Mapper
Read all stls to find overall bounding box, for camera position
Stl reader
Cut with plane
Mapper
Actor
Stl reader
Convert to vtkPolyData
Stl reader
Convert to vtkPolyData
Stl reader
Cut with plane
Mapper
Actor
Stl reader
Cut with plane
Mapper
Actor
Renderer
RenderWindow
Render to numpy array
Read all stls cut them individually and add actor to renderer
Most likely room for improvement.